## Slide 1
WIPRO NGA Program – 25SUB4505_5 G Developer
Capstone Project Presentation – 13th Feb 2026
www.rpsconsulting.in
Presented by – Group (03)
Project Title Here – 5G NR RLC ARQ Process

## Slide 2
Introduction
2024 - RPS Consulting all rights reserved
• 5G networks require ultra-reliable and low-latency data transmission for services like IoT, and video streaming. • The RLC layer ensures ordered and error-free delivery of data between PDCP and MAC layers. • ARQ mechanism helps in detecting packet loss and retransmitting missing data. • This project demonstrates ARQ working through C++ simulation.
Introduction

## Slide 3
2024 - RPS Consulting all rights reserved
• PDCP handles security, header compression, and data forwarding. • RLC performs segmentation, reassembly, and error control using ARQ. • MAC manages scheduling and fast retransmissions using HARQ. • PHY layer handles modulation, coding, and wireless transmission.
➡ RLC plays a key role in reliability.
5G Protocol Stack

## Slide 4
2024 - RPS Consulting all rights reserved
Layer 2 Protocol
Reliable Delivery
Retransmission
Flow Control
In-Order Delivery
Introduction to RLC ARQ
RLC Layer Overview
The Radio Link Control (RLC) layer is a critical component of the 5G NR protocol stack, positioned between PDCP and MAC layers.
RLC operates in three modes:
• Transparent Mode (TM)
• Unacknowledged Mode (UM)
• Acknowledged Mode (AM)
ARQ mechanism is implemented exclusively in AM mode, providing reliable data delivery through automatic retransmission of lost PDUs.
Key Highlights
Layer 2 Protocol
Reliable Delivery
Retransmission
Flow Control
In-Order Delivery

## Slide 5
2024 - RPS Consulting all rights reserved

## Slide 6
2024 - RPS Consulting all rights reserved
RLC Architecture Overview
Protocol Stack Position
PDCP Layer
Ciphering, Header Compression
RLC Layer
ARQ operates here
MAC Layer
Scheduling, HARQ
PHY Layer
Modulation, Coding
RLC AM Entity Structure
Transmitting Side
• SDU reception from PDCP
• PDU construction & segmentation
• Polling & retransmission
• STATUS processing
Receiving Side
• PDU reception & reordering
• Duplicate detection
• In-order delivery to PDCP
• STATUS report generation

## Slide 7
2024 - RPS Consulting all rights reserved

## Slide 8
2024 - RPS Consulting all rights reserved
ARQ Process Flow
1
SDU Reception
PDCP submits SDUs to RLC transmitter
2
PDU Construction
Build AMD PDUs with headers (D/C, P, SI, SN)
3
Polling
Set Poll bit based on triggers
4
Transmission
Submit to MAC layer for air interface
5
Reception
Receiver buffers and validates PDU
6
In-Order Delivery
Deliver consecutive PDUs to PDCP
7
STATUS Report
Generate ACK/NACK feedback
8
Retransmission
Retransmit NACKed PDUs

## Slide 9
2024 - RPS Consulting all rights reserved
C++ Implementation Overview
Step 1: Data Structures & Enums
PollBit, SDU, PDU, STATUS_PDU
Step 2: Configuration Parameters
RLC_AM_Config with 3GPP TS 38.331 compliance
Step 3: Transmitter Implementation
RLC_AM_Transmitter class with ARQ logic
Step 4: Receiver Implementation
RLC_AM_Receiver class with in-order delivery and STATUS generation
Step 5: Main Simulation
Complete ARQ process orchestration

## Slide 10
2024 - RPS Consulting all rights reserved
Key Data Structures
PollBit (Polling Field)
P_NOT_SET = 0
P_SET = 1
AMD_PDU_Header
SDU (Service Data Unit)
id : SDU identifier
size : Size of data from PDCP
STATUS_PDU (ARQ Feedback)
ack_sn : All SNs below this are acknowledged
nacks : List of missing SNs for retransmission
sn : Sequence Number
poll : Polling flag
size : SDU size
retx : Retransmission count

## Slide 11
2024 - RPS Consulting all rights reserved
RLC AM Configuration Parameters
Parameter | Value | Description
total_sdus | 8 | Number of SDUs submitted from PDCP
pollPDU | 4 | Trigger poll after every 4 PDUs
maxRetx | 3 | Maximum retransmission attempts
error_rate | 25% | Simulated channel packet loss rate

## Slide 12
2024 - RPS Consulting all rights reserved
Sample Code
www.cafetele.com
Specialized Training in:
4G/5G • O-RAN • AI/ML • Network Optimization
          Phase : 01
The enum keyword is used to create an enumeration named PollBit with two values, P_NOT_SET and P_SET, mapped to 0 and 1, which helps replace numeric values with meaningful names and improves readability.
The struct keyword is used to define custom data types. SDU contains two integers id and size to represent data identity and length. PDU stores a sequence number sn, a PollBit poll value, a size, and retx = 0 to initialize retransmissions.
STATUS contains an acknowledged sequence number ack_sn and a vector<int> nacks, where vector is a dynamic array that stores multiple integers.

## Slide 13
2024 - RPS Consulting all rights reserved
Sample Code
      Phase : 02
This section defines a Config structure that stores simulation settings like total data units, polling interval, maximum retransmissions, and error rate, with default values assigned using =. The statement Config cfg; creates an object to access these settings throughout the program.
The print_separator function formats the output using cout and endl, while const string& avoids unnecessary copying. The channel_success function uses bool and If conditions to simulate transmission failure for specific sequence numbers and returns true or false.

## Slide 14
2024 - RPS Consulting all rights reserved
Sample Code
        Phase : 03
This section defines the RLC_Transmitter class, which represents the sender side of communication. The private part stores internal data like tx_buffer for sent packets, retx_queue for retransmissions, and variables such as TX_SN and poll_counter to track sequence numbers and statistics, which are hidden from outside access.
The public part contains usable functions like build_pdu, which creates a PDU from an SDU and decides when to trigger polling. The const SDU& avoids copying data, bool& poll allows updating the poll flag, and the if condition checks the threshold and prints a message using cout.

## Slide 15
2024 - RPS Consulting all rights reserved
Sample Code
          Phase : 04
This section defines the RLC_Receiver class, which represents the receiving side. Inside the private section, map<int, PDU> rx_buffer stores incoming packets in sequence order. Variables like RX_NEXT, total_rx, and total_delivered track the expected next packet and statistics. Keeping these variables private ensures they are only modified inside the class.
The receive function processes incoming PDUs. It prints the received sequence number using cout, stores the packet in rx_buffer, and increases the counter using ++. The while loop checks if the next expected packet is available using count(). If available, it delivers the packet in order, removes it using erase(), updates RX_NEXT, and increases the delivered count.

## Slide 16
2024 - RPS Consulting all rights reserved
Sample Code
          Phase : 05
This section contains the main() function, which is the entry point of the C++ program. Execution always starts from int main(). The cout statements print the program title and description using formatted text. The vector<SDU> sdus creates a dynamic list to store all data units to be sent during the simulation.
Next, objects RLC_Transmitter tx and RLC_Receiver rx are created to handle sending and receiving operations. The variable total_delivered is used to track how many packets are successfully received. This section controls the overall flow of the program and connects all previous components to run the complete simulation.

## Slide 17
2024 - RPS Consulting all rights reserved
Sample Output
=================================
PHASE 1: SDU Submission from PDCP
=================================
[TX] SDU #0 received from PDCP (100 bytes)
[TX] SDU #1 received from PDCP (150 bytes)
================================
PHASE 2: Initial Transmission & Channel
================================
[TX] SDU #0 received from PDCP (100 bytes)
[TX] SDU #1 received from PDCP (150 bytes)
=================================== PHASE 3: STATUS Report Generation (ARQ)
=================================== [RX] STATUS PDU: ACK_SN=1, NACKs=[1,4]
[TX] Processing STATUS: ACK_SN=1
[TX] SN=0 ACKed - removed from buffer
[TX] SN=2 ACKed - removed from buffer
====================================
PHASE 4: ARQ Retransmissions
====================================
--- Retransmission Round 1 ---
[TX] Retransmitting SN=1 (attempt 1)
[CH] SN=1 >>> Successfully received
[RX] Received SN=1
[RX] Delivering SN=1 to PDCP (in-order)
[RX] Delivering SN=2 to PDCP (in-order)
[RX] Delivering SN=3 to PDCP (in-order)
==========================
PHASE 5: Simulation Statistics
==========================
+------------------------------+
| SIMULATION RESULTS |
+------------------------------+
| Total SDUs Submitted: 8 |
| Total PDUs Sent: 8 |
| Total Retransmissions: 2 |
| Total Polls Sent: 2 |
| PDUs Received (Rx): 8 |
| SDUs Delivered (PDCP): 8 |
| STATUS PDUs Sent: 2 |
| Channel Error Rate: 25% |
+------------------------------+
Simulation Results (25% packet loss)

## Slide 18
2024 - RPS Consulting all rights reserved
Advantages and Limitations
    Advantages
• Ensures reliable data delivery in lossy channels. • Follows 3GPP standard specifications. • Easy to modify parameters for experiments. • Improves understanding of 5G protocol behavior.
      Limitations
• Timers are logically simulated, not real-time. • HARQ mechanism is not included. • Graphical visualization is not available. • Only single-user scenario is implemented.

## Slide 19
2024 - RPS Consulting all rights reserved
RLC Failure & Recovery
Failure Trigger
When a PDU exceeds maxRetxThreshold retransmission attempts
RRC Recovery Procedures
1. Report RLC failure to RRC layer
2. Trigger Radio Link Failure (RLF) recovery
3. Attempt RRC re-establishment
4. Perform cell reselection if needed
5. Handover to different cell as last resort

## Slide 20
2024 - RPS Consulting all rights reserved
3 GPP Reference

## Slide 21
2024 - RPS Consulting all rights reserved
Key Takeaways
ARQ provides reliable delivery at RLC layer through retransmission
Polling mechanism ensures timely STATUS feedback
Window-based flow control prevents buffer overflow
In-order delivery guarantees correct SDU sequencing
Complements MAC HARQ for end-to-end reliability
Implementation follows 3GPP TS 38.322 specification

## Slide 22
2024 - RPS Consulting all rights reserved
Thank You
                Presented By Group : 03
                1. Jayavarshini G
                2. Harshinie M
                3. Yuvaraj P
                4. Shreyash Bhatt
                5. Vikas Srivastava